Impact of A Bus Rapid Transit System Along

Expressways in Metro Manila

Alexis M. FILLONE				  Chino Antonio Q. QUE

Associate Professor				  Undergraduate Student

Civil Engineering Department		  Civil Engineering Department

De La Salle University			  De La Salle University

2401 Taft Avenue, Manila			  2401 Taft Avenue, Manila

E-mail: alexis.fillone@dlsu.edu.ph		  E-mail: chinoque4@yahoo.com.ph

| Lorenzo Leon G. RABAT Undergraduate Student Civil Engineering Department De La Salle University 2401 Taft Avenue, Manila E-mail: chinoque4@yahoo.com.ph | Caila Jean C. MARCIAL Undergraduate Student Civil Engineering Department De La Salle University 2401 Taft Avenue, Manila E-mail: cailamarcial@yahoo.com |
| --- | --- |

Abstract: This study aims to analyze the impact of introducing a bus rapid transit along expressways linking Metro Manila to the different provinces along the North and South Luzon Expressways. Currently, provincial buses are the only mode of public transport on the expressways. These buses have terminals located within Metro Manila and are one of the factors contributing to congestion. Introducing other modes of transport such as high capacity vehicles which follow specific routes, with designated stop points and make use of a prioritized lane will help improve the current situation. The primary objective of this study was to assess the impact that the proposed BRT had in terms of traffic congestion, passenger travel time, mobility, ridership potential and pollution. The study made use of volume count and on board surveys to obtain data that were used as primary input in the transit modeling process to analyze the impact of the BRT system in the whole Metro Manila road network. The proposed design of the BRT system was then presented and was proven to have a positive impact in terms of traffic congestion, passenger travel time, mobility, ridership potential and pollution in Metro Manila.

Key Words: Bus Rapid Transit, Co-benefit analysis, Transport emissions